## Slide 1
FCC RF Exposure Guidelines
Controlled vs. Uncontrolled Exposure and Practical Ham-Radio Calculations
Notes: Opening: RF safety is part of responsible amateur-radio operation. This presentation explains the two FCC exposure categories and a practical way to estimate RF power density.

## Slide 2
1. Why RF Exposure Matters
RF energy can produce biological heating when exposure is sufficiently high.
FCC rules establish Maximum Permissible Exposure (MPE) limits.
Amateur operators are responsible for ensuring their stations comply with applicable RF exposure requirements.
Evaluation considers frequency, power, antenna gain, duty cycle, distance, and who can enter the RF field.
Notes: Explain that the goal is compliance, not fear of RF. The FCC limits are frequency-dependent and distinguish controlled from general-public exposure.

## Slide 3
2. Controlled vs. Uncontrolled Exposure
Controlled / Occupational: people know RF exposure is present and can exercise control over their exposure.
For amateur stations, qualifying household members may be evaluated under controlled limits when appropriate RF-safety information has been provided.
Uncontrolled / General Population: people may be unaware of the RF field or unable to control their exposure.
Neighbors, visitors, pedestrians, and other nearby members of the public generally require the uncontrolled limits.
Notes: FCC Part 97 ties amateur stations to the RF exposure requirements. Emphasize that simply being a licensed ham does not automatically make every person in the area a controlled-exposure person.

## Slide 4
3. MPE: Maximum Permissible Exposure
At common amateur frequencies, compliance is often evaluated using power density.
Power density is commonly expressed in mW/cm².
The allowable MPE depends on frequency and exposure category.
Controlled limits are generally less restrictive than uncontrolled limits because exposed people are informed and able to control exposure.
Use the current FCC §1.1310 table for the exact limit at the operating frequency.
Notes: Do not memorize one universal number: the MPE limit changes with frequency. For a formal station evaluation, consult the current FCC table.

## Slide 5
FCC MPE Limits at Common HF Amateur Frequencies
Ham band | Example freq. | Controlled MPE | Uncontrolled MPE
160 m | 1.9 MHz | 100.00 mW/cm² | 49.86 mW/cm²
80 m | 3.75 MHz | 64.00 mW/cm² | 12.80 mW/cm²
60 m | 5.35 MHz | 31.44 mW/cm² | 6.29 mW/cm²
40 m | 7.15 MHz | 17.60 mW/cm² | 3.52 mW/cm²
30 m | 10.125 MHz | 8.78 mW/cm² | 1.76 mW/cm²
20 m | 14.2 MHz | 4.46 mW/cm² | 0.89 mW/cm²
17 m | 18.1 MHz | 2.75 mW/cm² | 0.55 mW/cm²
15 m | 21.2 MHz | 2.00 mW/cm² | 0.40 mW/cm²
12 m | 24.94 MHz | 1.45 mW/cm² | 0.29 mW/cm²
10 m | 28.4 MHz | 1.12 mW/cm² | 0.22 mW/cm²
Representative frequencies shown. HF limits from 3–30 MHz vary as 1/f², so use the actual transmit frequency for a station evaluation.
Notes: These values are power-density MPE limits in mW/cm², calculated from FCC §1.1310 using a representative frequency in each amateur band. Controlled exposure is averaged over 6 minutes; general-population/uncontrolled exposure over 30 minutes.

## Slide 6
Duty Cycle Overview
The duty cycle refers to the percentage of time a transmitter is active during a transmission period. Different modes of communication in amateur radio have varying duty cycles, which can significantly impact equipment performance and longevity.
Duty Cycle Comparisons
Transmission Mode
Duty Cycle
SSB (Single Side Band)
20%
CW (Continuous Wave)
50%
Digital Modes (e.g., FT8)
Nearly 100%

## Slide 7
4. First Calculate Average Transmitter Power
RF exposure is based on time-averaged exposure, so operating mode and transmit time matter.
Average power ≈ Transmitter Power × Duty Cycle.
Example: 100 W transmitter at 50% transmit duty cycle → 100 × 0.50 = 50 W average.
If a mode transmits only 20% of the averaging period → 100 × 0.20 = 20 W average.
Use a realistic, defensible duty cycle for the operating mode and station.
Notes: Duty cycle can substantially change the calculated exposure. Continuous-duty digital modes can require more conservative assumptions than intermittent voice operation.

## Slide 8
5. Include Antenna Gain and Feed-Line Loss
Convert antenna gain from dB to a linear power ratio:
Gain ratio = 10^(Gain_dB / 10)
Example: 6 dB gain → 10^(6/10) ≈ 3.98.
A useful estimate of effective radiated power is: P × duty cycle × gain ratio × feed-line efficiency.
Be careful whether antenna gain is specified in dBi or dBd.
Notes: Point out that 3 dB is approximately a factor of 2 in power and 6 dB approximately a factor of 4. Feed-line loss reduces power reaching the antenna.

## Slide 9
6. Estimating Power Density
A common far-field estimate is:
S = (P × G) / (4πR²)
S = power density; P = average power at the antenna; G = linear antenna gain; R = distance.
For a directional antenna, evaluate locations where people can be exposed to the strongest portion of the pattern.
Near-field conditions and complex installations may require more detailed methods or measurements.
Notes: This inverse-square estimate is useful for teaching and many simplified evaluations, but antennas are not ideal point sources and the near field needs special consideration.

## Slide 10
7. Worked Example: 100 W Station
Assume: 100 W transmitter, 50% duty cycle, 3 dB antenna gain, negligible feed-line loss.
1) Average power: 100 W × 0.50 = 50 W
2) 3 dB gain ratio: 10^(3/10) ≈ 2.0
3) Effective average radiated power ≈ 50 W × 2 = 100 W
4) At 5 m: S ≈ 100 / [4π(5²)] = 0.318 W/m²
5) Convert units: 1 W/m² = 0.1 mW/cm²
Therefore S ≈ 0.0318 mW/cm²
6) Compare 0.0318 mW/cm² with the applicable FCC MPE limit for that frequency.
Notes: Walk through the arithmetic. The final step is always comparison with the FCC limit at the actual operating frequency and for the appropriate exposure category.

## Slide 11
8. Solving for a Minimum Distance
If the applicable MPE limit is known, rearrange the equation:
R = √[(P × G) / (4πS_limit)]
Use consistent units throughout the calculation.
Calculate separately when controlled and uncontrolled MPE limits differ.
The uncontrolled calculation is especially important for property lines, sidewalks, neighboring homes, and visitor-accessible areas.
Notes: Explain that distance is one of the easiest ways to reduce exposure because power density falls rapidly as distance increases.

## Slide 12
9. Multiple Bands and Multiple Transmitters
A station may operate on several bands with different FCC MPE limits.
Evaluate the bands and operating conditions that can produce the greatest exposure.
Simultaneous RF sources may need a combined-exposure evaluation.
A common compliance approach is to sum each source's fractional contribution to its applicable limit.
If station equipment, antennas, power, or accessible areas change, reconsider the evaluation.
Notes: This slide is important for multi-transmitter stations, repeaters, contest stations, and sites with more than one RF source.

## Slide 13
10. Practical Ways to Reduce Exposure
Increase the distance between people and the antenna.
Raise or relocate the antenna so high-field areas are inaccessible.
Reduce transmitter power when full power is unnecessary.
Reduce transmit duty cycle where operationally appropriate.
Use barriers, signs, or access restrictions where needed.
Account for antenna directionality and avoid aiming high-gain antennas toward occupied areas at close range.
Notes: Most compliance problems can be addressed through ordinary station design: distance, antenna placement, power management, and access control.

## Slide 14
11. Key Takeaways
Know whether each potentially exposed person falls under controlled or uncontrolled limits.
Determine frequency, transmitter power, duty cycle, feed-line loss, antenna gain, and distance.
Estimate power density or use an FCC-recognized evaluation method.
Compare the result with the applicable FCC MPE limit.
Document the evaluation and revisit it when the station changes.
When in doubt, use conservative assumptions or obtain a more detailed RF evaluation.
Notes: Close by emphasizing that RF exposure evaluation is a normal part of station engineering and responsible amateur operation.

## Slide 15
12. FCC References
47 CFR §97.13(c) — Amateur station RF exposure responsibility.
47 CFR §1.1310 — FCC radiofrequency exposure limits.
47 CFR §1.1307 — Actions that may have significant environmental effects; RF exposure evaluation provisions.
FCC OET Bulletin 65 — Guidance for evaluating compliance with RF exposure limits.
FCC OET Knowledge Database — Current RF exposure guidance and procedures.
Notes: Encourage the audience to use current FCC rules and guidance rather than relying only on old handouts or memorized tables.

## Slide 16
FCC MPE Limits at Common VHF/UHF/Microwave Frequencies
Ham band | Example freq. | Controlled MPE | Uncontrolled MPE
6 m | 50.1 MHz | 1.00 mW/cm² | 0.20 mW/cm²
2 m | 146 MHz | 1.00 mW/cm² | 0.20 mW/cm²
1.25 m | 223.5 MHz | 1.00 mW/cm² | 0.20 mW/cm²
70 cm | 440 MHz | 1.47 mW/cm² | 0.29 mW/cm²
33 cm | 915 MHz | 3.05 mW/cm² | 0.61 mW/cm²
23 cm | 1296 MHz | 4.32 mW/cm² | 0.86 mW/cm²
13 cm | 2304 MHz | 5.00 mW/cm² | 1.00 mW/cm²
9 cm | 3456 MHz | 5.00 mW/cm² | 1.00 mW/cm²
5 cm | 5760 MHz | 5.00 mW/cm² | 1.00 mW/cm²
3 cm | 10368 MHz | 5.00 mW/cm² | 1.00 mW/cm²
30–300 MHz: 1.0 controlled / 0.2 uncontrolled. From 300–1500 MHz the limits rise with frequency; above 1500 MHz they are 5.0 / 1.0 mW/cm².
Notes: These values are power-density MPE limits in mW/cm², calculated from FCC §1.1310 using a representative frequency in each amateur band. Controlled exposure is averaged over 6 minutes; general-population/uncontrolled exposure over 30 minutes.

## Slide 17
FCC §1.1310 MPE Power-Density Formulas
Occupational / Controlled — averaging time: 6 minutes
0.3–3 MHz: 100 mW/cm² | 3–30 MHz: 900/f² | 30–300 MHz: 1.0
300–1500 MHz: f/300 | 1500–100,000 MHz: 5.0 mW/cm²
General Population / Uncontrolled — averaging time: 30 minutes
0.3–1.34 MHz: 100 mW/cm² | 1.34–30 MHz: 180/f² | 30–300 MHz: 0.2
300–1500 MHz: f/1500 | 1500–100,000 MHz: 1.0 mW/cm²
f = frequency in MHz. For formal compliance, use the actual frequency and current FCC rules.
Notes: This slide gives the FCC power-density equations used to calculate the representative amateur-band values in the preceding tables.

## Slide 18
Illustrative Minimum Compliance Distance — HF (100 W)
Band | Freq. | Controlled MPE | Controlled min. | Uncontrolled min.
160 m | 1.9 MHz | 100.00 mW/cm² | 0.29 ft | 0.41 ft
80 m | 3.75 MHz | 64.00 mW/cm² | 0.37 ft | 0.82 ft
60 m | 5.35 MHz | 31.44 mW/cm² | 0.52 ft | 1.17 ft
40 m | 7.15 MHz | 17.60 mW/cm² | 0.70 ft | 1.56 ft
30 m | 10.125 MHz | 8.78 mW/cm² | 0.99 ft | 2.21 ft
20 m | 14.2 MHz | 4.46 mW/cm² | 1.39 ft | 3.10 ft
17 m | 18.1 MHz | 2.75 mW/cm² | 1.77 ft | 3.95 ft
15 m | 21.2 MHz | 2.00 mW/cm² | 2.07 ft | 4.62 ft
12 m | 24.94 MHz | 1.45 mW/cm² | 2.43 ft | 5.44 ft
10 m | 28.4 MHz | 1.12 mW/cm² | 2.77 ft | 6.20 ft
Illustrative far-field estimate: 100 W at antenna, 0 dBi gain, 100% duty cycle, no added ground-reflection factor. Actual compliance distance depends on the station.
Notes: These are illustrative minimum compliance distances, not universal distances for each band. They use the simple far-field equation with 100 watts at the antenna, unity gain, and continuous transmission. A real evaluation must use actual power at the antenna, gain, duty cycle, transmit/receive pattern, frequency, antenna pattern and, where appropriate, ground reflection. ARRL's calculator can be used for station-specific results.

## Slide 19
Illustrative Minimum Compliance Distance — VHF/UHF (100 W)
Band | Freq. | Controlled MPE | Controlled min. | Uncontrolled min.
6 m | 50.1 MHz | 1.00 mW/cm² | 2.93 ft | 6.54 ft
2 m | 146 MHz | 1.00 mW/cm² | 2.93 ft | 6.54 ft
1.25 m | 223.5 MHz | 1.00 mW/cm² | 2.93 ft | 6.54 ft
70 cm | 440 MHz | 1.47 mW/cm² | 2.42 ft | 5.40 ft
33 cm | 915 MHz | 3.05 mW/cm² | 1.68 ft | 3.75 ft
23 cm | 1296 MHz | 4.32 mW/cm² | 1.41 ft | 3.15 ft
13 cm | 2304 MHz | 5.00 mW/cm² | 1.31 ft | 2.93 ft
9 cm | 3456 MHz | 5.00 mW/cm² | 1.31 ft | 2.93 ft
5 cm | 5760 MHz | 5.00 mW/cm² | 1.31 ft | 2.93 ft
3 cm | 10368 MHz | 5.00 mW/cm² | 1.31 ft | 2.93 ft
Illustrative far-field estimate: 100 W at antenna, 0 dBi gain, 100% duty cycle, no added ground-reflection factor. Actual compliance distance depends on the station.
Notes: These are illustrative minimum compliance distances, not universal distances for each band. They use the simple far-field equation with 100 watts at the antenna, unity gain, and continuous transmission. A real evaluation must use actual power at the antenna, gain, duty cycle, transmit/receive pattern, frequency, antenna pattern and, where appropriate, ground reflection. ARRL's calculator can be used for station-specific results.

## Slide 20
How to Calculate Minimum Compliance Distance
Use the applicable FCC MPE limit and solve the far-field power-density equation for distance:
R = √[(P × G) / (4πSlimit)]
P = time-averaged power at the antenna in watts
G = antenna gain as a linear ratio (0 dBi = 1.0; 3 dBi ≈ 2.0)
Slimit = applicable controlled or uncontrolled MPE converted to W/m²
Conversion: 1 mW/cm² = 10 W/m²
Example — 146 MHz, 100 W, 0 dBi, 100% duty:
Controlled MPE 1.0 mW/cm² → about 2.93 ft (0.89 m)
Uncontrolled MPE 0.2 mW/cm² → about 6.54 ft (1.99 m)
Notes: Stress that 'minimum safe distance' is better described as minimum compliance distance. There is no single distance for a ham band because power, antenna gain, duty cycle and installation differ. The ARRL calculator also allows ground reflections to be included and should not be used for antennas within 20 cm of a person.